## Slide 1: AstroEngr 331X
The Space Environment:
Freefall & Vaccuum
May 2024

## Slide 2: Free Fall Environment
NOT “Zero Gravity”

## Slide 3: Free Fall Environment
Effects on Spacecraft
  Useful:
    No contact forces – structural loads are minimal
  Problematic:
    Fluid measurement and delivery are more difficult
Fuel

## Slide 4: Earth’s Atmosphere
https://www.esa.int/ESA_Multimedia/Images/2009/06/Atmospheric_density_changes_with_altitude

## Slide 5: Atmospheric Drag
Drag
  Difficult to predict
  Can lead to re-entry/end of mission
  Negligible above ~600 km
Impact on satellite design:
  Lower bound on orbital altitude
  Propulsion system must be designed to counteract drag
  Shape/orientation can be designed to have desired properties
    Differential drag for formation flying

## Slide 6: Atomic Oxygen
Impact on satellite design:
Atomic Oxygen
  At high altitude, O2 molecules are split by radiation and charged particles
  Low density leads to atomic oxygen (“O”) persisting rather than immediately recombining to molecular form
  “O” can
    Weaken structures through oxidation
    Change properties of coatings
    Degrade sensors
  Materials must be chosen to limit these effects
Notes: Skylab example

## Slide 7: Near-Vacuum
Effect Description Design Impact
The lack of a dense atmosphere in space also impacts spacecraft design!
No O2 to enable combustion
Propulsion system cannot rely on atmospheric oxygen
Oxidizer must be carried on-board if relying on chemical means of propulsion
Outgassing
Materials release trapped gases
Choose materials carefully, thermal-vac testing prior to launch
Cold welding
No “air pocket” between moving parts
Try to limit moving parts
Limited heat transfer
Radiation is the only method to transfer heat into/out of the spacecraft
Thermal system and materials must be designed carefully balance radiative heat transfer in/out
Notes: Can use to our advantage.

## Slide 8: Near-Vacuum: Impact on spacecraft motion
Spacecraft cannot utilize contact with external mass to accelerate or rotate
To accelerate (or rotate) spacecraft must expel mass or exchange energy